## Slide 1: Julian Lüken
Avid lover of all things Computer Science and Math.

## Slide 2: About me
M. Sc. Applied Computer Science
  Areas of specialization: Scientific Computing, Digital Signal Processing
Currently working at the German Aerospace Center (since 2021)
  Institute of Propulsion Technology, Turbine Department in Göttingen (DE)
  Thesis project CoolingGen
Knowledge and interest in math and programming, especially w.r.t. Digital Signal Processing
Lucky enough to throroughly enjoy math courses dedicated to Computer Tomography

## Slide 3: CoolingGen
State-of-the-art tool for parametric modelling of 3D turbine blade/vane geometries at the German Aerospace Center
Based on custom CAD kernel
Uses NURBS for object representation
Uses streamsurface coordinate transformation coupled with custom algorithms (fillet creation, ray marching, …) for fast geometry modification

## Slide 4: CoolingGen
Problem: Aviation cooling structures are hard to model with conventional CAD tools. Once they are created, they are hard to modify
Solution: Make own CAD tool that has its own primitives based on (relatively) simple parameter representations. We can then simply modify the input and re-create the geometry

## Slide 5: CoolingGen
Problem 2: Resulting shapes are intersection-heavy. Using Boolean operators, this will take ages to generate. No can do!
Solution 2: Use more simple representations of the shapes and find a way to intersect these.

## Slide 6
Offset delimiting curves
Trim at intersections
Add fillets
Fillet creation process
Transform to streamsurface
coordinate system

## Slide 7
Inverse transform (black curves) and surface lifting (orange surface)

## Slide 8
Creating turns between the resulting channels
Fuse channels, find plane intersections
Once again, surface lifting

## Slide 9
Multiple turns

## Slide 10
Hole creation
Basic 2D curves
In this case: circle, rounded rectangle
Embed in 3D space using line segment
Find special linearly interpolated surface

## Slide 11
Hole intersection
The orange shape consists of rays, which are much easier to intersect with surface than surfaces
Notice:

## Slide 12
Hole intersection with ray marching
Original shape
Ray marching
Intersected shape

## Slide 13: Resulting surfaces

## Slide 14: Resulting solids

## Slide 15: Resulting CFD Simulation

## Slide 16: Computer Tomography in 2D – The Radon transform
X-rays traversing a small distance suffer a relative intensity loss:
Beam is strongly focused  Assume line:
Set up differential equation:
Integrate along line to find:
Which is where we get the Radon transform R from:

## Slide 17: Essential task in CT
We want to reconstruct the density function from its‘ Radon transform (or in n-dimensional space, the John transform)
But: Analytic inversion not feasible, many different factors:
  Only sometimes actually invertible
  Non-locality of solution
  …
Many approaches to approximate solution…
  Algebraic reconstruction technique
  Cormack inversion formula
  Filtered back projection
  Fourier reconstruction
  …

## Slide 18: Also about me
I enjoy cooking, hiking and video games
Playing the guitar for 15 years now
Loves Jazz and Progressive Metal